## Slide 1
OPEN INNOVATION
Leaf Sync - Smart
Monitoring System
A hidden IoT-based personal safety device disguised as a decorative plant

## Slide 2
01
The Problem
Phones unreachable
Hard to grab during a sudden threat
Visible panic buttons
Easily spotted and disabled by attackers
No evidence collected
Traditional alerts don't record what happened
Complex activation
Multi-step apps fail when speed matters
The Core Gap
No existing system combines hidden activation, instant alerting, and audio evidence in a single discreet device.
Who it affects
Women at home, hostels, PGs
Elderly individuals living alone
Anyone in an indoor emergency

## Slide 3
02
Our Solution
A smart safety system hidden inside an artificial flower pot
Discreet Design
Looks exactly like a decorative pot. No one suspects a thing.
Two-Step Activation
Tap the pot → touch the secret leaf. Dual-trigger prevents false alarms.
Instant Alert
Sends emergency notification to the Blynk app via Wi-Fi in seconds.
Audio Evidence
INMP441 mic records surroundings. Saved to SD card for later use.
Dual Controllers
ESP32 handles recording. ESP8266 handles alerting. No bottleneck.
No App Needed to Trigger
Simple physical gestures activate the system — even in panic.

## Slide 4
03
How It Works
1
Tap the Pot
Vibration sensor detects knock — Step 1 activated
2
Touch the Leaf
Hidden capacitive sensor confirms — Step 2 done
3
Alert Sent
ESP8266 fires notification to Blynk app via Wi-Fi
4
Audio Recorded
ESP32 captures surroundings via I2S mic to SD card
ESP8266 → Alert & Notification
ESP32 → Audio Recording & SD Storage

## Slide 5
04
Technology Stack
HARDWARE
ESP32 DevKit V1
Main controller — audio + SD
NodeMCU ESP8266
Wi-Fi alerts via Blynk
Vibration Sensor
Tap detection — Step 1 trigger
Capacitive Touch Sensor
Leaf touch — Step 2 trigger
INMP441 Microphone
I2S digital audio recording
MicroSD Module (32GB)
Evidence storage via SPI
SOFTWARE
Arduino IDE
Embedded C for ESP32 & ESP8266
Blynk IoT Platform
Real-time mobile alert delivery
I2S Protocol
High-quality digital audio input
SPI Protocol
SD card read/write interface
Wi-Fi (802.11)
Cloud communication layer
Cirkit Designer
Circuit design & simulation

## Slide 6
05
Project Implementation
ESP32 DevKit V1
NodeMCU ESP8266
Vibration Sensor
Capacitive Touch Sensor
INMP441 Microphone
Prototype
Simulated setup

## Slide 7
06
Why This Stands Out
Feature Comparison
Feature
Panic Buttons
Safety Apps
Our System
Hidden / Discreet
✗
✗
✓
No phone needed
✓
✗
✓
Audio Evidence
✗
✗
✓
False-alarm prevention
✗
Limited
✓
Works offline (partial)
✓
✗
✓
Low cost
✗
✓
✓
Best for: Homes · Hostels · PG Accommodations · Elderly Care · Any Indoor Emergency

## Slide 8
What's Next
GPS Integration
Send live location with the alert for faster rescue
Cloud Audio Backup
Upload recordings to cloud for remote retrieval
AI Distress Detection
Auto-trigger using sound pattern recognition
Mobile App
Custom dashboard for alert history and settings
Safety should be invisible — and always within reach.